## Slide 1: How does MeDeHa interfaces with MANET and DTN2 networks

## Slide 2
MeDeHa
Routing Table
Ethernet
Wi-Fi
MeDeHa powered Infrastructure Network
MANET Network managed by OLSR
1: Packet Received
2: MeDeHa
extracts
Data and @
Gateway Node (Interfacing with a MANET network)
6
MeDeHa + OLSR Interface
4: MeDeHa asks
For forwarding
The packet
3: MeDeHa verifies
the existence
of the MANET destination
5: Injects
The packet towards the
Selected destination
6: OLSR updates
The MANET routing table

## Slide 3
MeDeHa
Collected EID(s)
HBSD External Router
Ethernet
Wi-Fi
MeDeHa powered Infrastructure Network
DTN2 Daemon
DTN2 + HBSD Powered Mobile Network
1: Packet Received
2: MeDeHa extracts
Data and @
3: MeDeHa verifies
the existence
of the DTN destination
5: DTN2 injects
The new Bundle towards the
Selected destination
Gateway Node (Interfacing with a DTN network)
6
6: HBSD updates
The list of available
EID(s) whenever it
Receives a notification
from DTN2 about the
Existence of a new
DTN Node.
4: MeDeHa asks
For Bundling and
Sending the
data

## Slide 4: Connection of HBSD external router to the DTN2 daemon
Maintain/ Exchange Network Statistics
Make Decisions (Scheduling, Drop, Forwarding)
Maintain Network Description (Nodes, Links, …)
Receive events via a Multicast channel (XML-SAX)
Send
Requests vi a Multicast Channel
Load Configuration
Save Log
Manage local, persistent storage of bundles
DTN2 Daemon
HBSD External Router